## Slide 1
Group 4
Life Cycle Engineeing Case Study : Pressure Cooker Lid
Guided by - Prof. Dr. Paulo Pecas
M.Sc. Advanced Manufacturing Course
Technische Universität Chemnitz
July 2024
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
1
MEET THE TEAM
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
MEET THE TEAM
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas

## Slide 2
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
2
CONTENTS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
PRODUCT PITCH
01.
MARKET RESEARCH
02.
03.
MACHINE CALCULATION
04.
COST ANALYSIS
05.
SENSITIVITY ANALYSIS

## Slide 3
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
3
CONTENTS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
LIFE CYCLE IMPACT ANALYSIS
06.
FUNCTIONAL ASSESSMENT
07.
08.
USE PHASE ANALYSIS
09.
TERNARY DIAGRAM
10.
SUMMARY

## Slide 4
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
4
Selected Product
PRODUCT PITCH
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas

## Slide 5
PRODUCT PITCH
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
5
Projected Surface Area
Material | Steel
Surface Area | 178000 mm2
Projected Area | 80777 mm2
Thickness | 1 mm
Production Type | Blanking and Stamping
Total Material Required(per year) | 8424323.625 Kg
Material | Aluminium
Surface Area | 186000 mm2
Projected Area | 80777 mm2
Thickness | 2.6 mm
Production Type | Blanking and Stamping
Total Material Required(per year) | 6690061.823 Kg
Material | Unit Cost (EUR/Kg) | Scrap Cost (EUR/Kg) | EI'99 Material Prod | EI'99 EOL | σR | σyeild | Density [kg/m3]
Al | 2.52 | -1.44 | 0.7 | Recycle -57010-3 | 290 | 170 | 2712
Steel | 0.72 | -0.17 | 0.55 | Recycle -9610-3 | 700 | 350 | 900
Material | Unit Cost (EUR/Kg) | Scrap Cost (EUR/Kg) | EI'99 Material Prod | EI'99 EOL | σR | σyeild | Density [kg/m3]
Al | 2.52 | -1.44 | 0.7 |  | 290 | 170 | 2712
Steel | 0.72 | -0.17 | 0.55 |  | 700 | 350 | 900

## Slide 6: Reduce presentation size
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
MATERIAL COMPARISON
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Aluminum
Steel
6

## Slide 7
Durability
Stainless steel pressure cookers are generally more durable, resistant to scratches, dents, and corrosion and long-lasting than their aluminum counterparts, which can be prone to denting and warping over time.
Heat Conductivity
Aluminum pressure cookers heat up quickly and evenly resulting into and therefore, lesser fuel consumption, while stainless steel may take a bit longer to reach the desired temperature.
Maintenance
Stainless steel pressure cookers are easier to clean and maintain, with a smooth, non-porous surface that resists staining and odors. Aluminum can be more prone to discoloration and stains.
COMPARISON OF FEATURES
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
7
Aluminum VS Steel

## Slide 8
Cost
Aluminium pressure cookers are generally more affordable than their steel counterparts, but their longevity often make them a cost-effective choice in the long run.
Lightweight and Portable
Aluminum pressure cookers are known for their lightweight and portable design, making them easy to move around the kitchen or even take with you when traveling.
COMPARISON OF FEATURES
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
. Stainless Steel
8
Chart: Comparison
| Weight | Usability | Heat distribution | Cost | Cleaning | Durability | Scratch resistance | Reactivity
Rating of aspects in materials Aluminium | -0.9 | -0.8 | -0.9 | -0.6 | -0.6 | -0.6 | -0.5 | -0.5
Rating of aspects in materials steel | 0.5 | 0.7 | 0.7 | 0.8 | 0.9 | 0.9 | 0.9 | 1

## Slide 9
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
9
Sales volume of Pressure cookers in European market 34 million Nos per year.
Aluminum - 40% of the overall pressure cooker market in Europe. 13.6 million
Steel - 60% of the overall pressure cooker market in Europe. 20.4 million
We are targeting 10 million Nos. of market share of both Steel and Aluminum
Material | Average Price (EUR)
Aluminum | € 3
Steel | € 2
Source: Fortunebuissnessinsights.com
EFFECTIVE PRODUCTION VOL.
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas

## Slide 10
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
10
Thickness Definition
Using Hoop Stress Formula:
P=1.2 atm/ 0.1214 Mpa
r= 0.15m,
Steel
Aluminum
t ≈ 1 mm
t ≈ 2.6 mm
For Practical purposes, durability and manufacturing feasibility the min thickness for steel 1mm is more reasonable for such application which leads to FOS of 13.5.
2.6 mm
1 mm
EFFECTIVE PRODUCTION VOL.
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas

## Slide 11
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
11
Steel
D = 320.7 mm
T = 1 mm
= (3.14 * 320.7 * 1)*
= 528942.10 N
= 54 tonne
No. of parts to stamp in 1 sheet 25 Nos, (5x5)
EFFECTIVE PRODUCTION VOL.
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas

## Slide 12
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
12
Aluminum
D = 320.7 mm
T = 2.6 mm
= (3.14 * 320.7 * 2.6)*
= 602490.24 N
= 62 tonne
No. of parts to stamp in 1 sheet 20 Nos, (4x5)
EFFECTIVE PRODUCTION VOL.
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas

## Slide 13
EFFECTIVE PRODUCTION VOL.
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
13
Target Production Volume
10,000,000
Effective Production Volume
10,025,063
Effective Production Volume
10,030,078
PROCESS
PROCESS
STAMPING
Blanking
REJECTION = 0.25%
REJECTION = 0.05%
Effective PRODUCTION VOLUME
TOOL COST CALCULATION
Tool Cost = A * (nr hits)B (Surf Area/Proj Area)C (Part Width*Part Length)D
= 1567 x (4)1.366 x (73/18.68)0.323 x (64 x 124.160)0.342
= 25,241 Euros
Tool Cost = A * (nr hits)B (Surf Area/Proj Area)C (Part Width*Part Length)D
= 1567 x (4)1.366 x (73/18.68)0.323 x (64 x 124.160)0.342
= 25,602 Euros

## Slide 14
UNIT COST ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Steel
Total force = F (for 1 part) x No. of Parts
= 54 x 25
= 1350 Tonne
Which is lower << 2100 Machine No.1,
Therefore machine 1 is selected.
Aluminum
Total force = F (for 1 part) x No. of Parts
= 60 x 20
= 1200 Tonne
Which is lower << 2100 Machine No.1,
Therefore machine 1 is selected.
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
14
Selection of Stamping Machine (Steel and Aluminum)

## Slide 15
UNIT COST ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Steel and Aluminum
Aluminum
P = 2l + 2b
= 2 1635.5+2 1311.8
= 5895 mm
= (0.8 290 5895 2.6)
= 3555864 N
= 362.6 Tonne
Steel
P = 2l + 2b
= 2 1635.5+2 1635.5
= 6524 mm
= (0.8 700 6524 1)
= 3663520 N
= 373.57 Tonne
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
15

## Slide 16
UNIT COST ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Selection of Blanking Machine
Based on the blanking calculation total required force for Steel is 373.57 Tonne and for Aluminum is 362.6 Tonne
So Machine 1 is selected.
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
16

## Slide 17
COST ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Variable Cost | Unit Cost | Per Year | Percent
Material Cost | € 0.605 | € 60,65,513 | 61.9%
Energy Cost | € 0.009 | € 91,296 | 0.93%
Labour Cost | € 0.003 | € 27,440 | 0.28%
Total Variable Cost | € 0.617 | € 61,84,249 | 63%
Fixed Cost | Unit Cost | Per Year | Percent
Main Machine Cost+Interest | € 0.189 | € 18,92,895 | 19%
Auxiliary Equipment Cost | € 0.053 | € 5,31,405 | 5%
Tooling Cost | € 0.003 | € 25,241 | 0%
Fixed Overhead | € 0.087 | € 8,73,331 | 9%
Building Cost | € 0.005 | € 45,690 | 0%
Maintenance Cost | € 0.025 | € 2,49,523 | 3%
Total Fixed Cost | € 0.362 | € 36,18,085 | 37%
Total Cost | € 0.978 | € 98,02,335 | 100%
Steel
Chart: Steel
| Material Cost | Energy Cost | Labour Cost | Main Machine Cost+Interest | Auxiliary Equipment Cost | Tooling Cost | Fixed Overhead | Building Cost | Maintenance Cost
 | 0.60473 | 0.0091022 | 0.0027358 | 0.18929 | 0.053141 | 0.0025241 | 0.087333 | 0.004569 | 0.024952
Chart: Steel
| Total Variable Cost | Total Fixed Cost
 | 0.61657 | 0.36181
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
17

## Slide 18
COST ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Variable Cost | Unit Cost | Per Year | Percent
Material Cost | € 1.681 | € 1,68,58,956 | 81.7%
Energy Cost | € 0.011 | € 1,12,783 | 0.55%
Labour Cost | € 0.003 | € 34,300 | 0.17%
Total Variable Cost | € 1.696 | € 1,70,06,039 | 82%
Fixed Cost | Unit Cost | Per Year | Percent
Main Machine Cost+interest | € 0.189 | € 18,92,895 | 9%
Auxiliary Equipment Cost | € 0.053 | € 5,31,405 | 3%
Tooling Cost | € 0.003 | € 25,602 | 0%
Fixed Overhead | € 0.087 | € 8,73,457 | 4%
Building Cost | € 0.005 | € 45,690 | 0%
Maintenance Cost | € 0.025 | € 2,49,559 | 1%
Total Fixed Cost | € 0.362 | € 36,18,609 | 18%
Total Cost | € 2.057 | € 2,06,24,648 | 100%
Aluminum
Chart: Aluminum
| Material Cost | Energy Cost | Labour Cost | Main Machine Cost+interest | Auxiliary Equipment Cost | Tooling Cost | Fixed Overhead | Building Cost | Maintenance Cost
 | 1.6808 | 0.011244 | 0.0034198 | 0.18929 | 0.053141 | 0.0025602 | 0.087346 | 0.004569 | 0.024956
Chart: Aluminum
| Total Variable Cost | Total Fixed Cost
 | 1.6955 | 0.36186
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
18

## Slide 19
Material | Energy Cost | Material Cost | Labour cost | Variable Cost/Unit | Fixed Cost/Unit | Total Cost/Unit
Steel | € 91,296 | € 6,065,513 | € 27,440 | € 0.617 | € 0.349 | € 0.978
Aluminum | € 112,374 | € 16,858,956 | € 33,279 | € 1.695 | € 0.349 | € 2.045
UNIT COST = FIXED COST/UNIT + VARIABLE COST/UNIT
Variable Cost/Unit = Material Cost + Energy Cost + Labour Cost
Effective Production Volume
Fixed Cost/Unit = Machine Cost + Auxiliary & Installation Cost + Tool Cost + Building Cost
Effective Production Volume
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
19
COST ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas

## Slide 20
VARIATION OF TOTAL COSTS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Chart: VARIATION OF TOTAL COSTS (STEEL)
Variable Cost | 0.61842 | 1855274.7953 | 3710549.5907 | 5565824.386 | 7421099.1813 | 9276373.9766 | 11131648.772 | 12986923.5673 | 14842198.3626 | 16697473.1579 | 18552747.9533 | 20408022.7486 | 22263297.5439 | 24118572.3392 | 25973847.1346 | 27829121.9299 | 29684396.7252 | 31539671.5206
Fixed Cost | 3618085.4263 | 3618085.4263 | 3618085.4263 | 3618085.4263 | 3618085.4263 | 5854676.9646 | 5854676.9646 | 5854676.9646 | 5854676.9646 | 5854676.9646 | 8091268.5029 | 8091268.5029 | 8091268.5029 | 8091268.5029 | 10327860.0412 | 10327860.0412 | 10327860.0412 | 10327860.0412
Total Cost | 3618086.0447 | 5473360.2216 | 7328635.0169 | 9183909.8123 | 11039184.6076 | 15131050.9412 | 16986325.7366 | 18841600.5319 | 20696875.3272 | 22552150.1225 | 26644016.4562 | 28499291.2515 | 30354566.0468 | 32209840.8422 | 36301707.1758 | 38156981.9711 | 40012256.7664 | 41867531.5618
Chart: VARIATION OF TOTAL COST (ALUMINIUM)
Variable Cost | 1.7007 | 5102212.8534 | 10204425.7068 | 15306638.5602 | 20408851.4135 | 25511064.2669 | 30613277.1203 | 35715489.9737 | 40817702.8271 | 45919915.6805 | 51022128.5339 | 56124341.3873 | 61226554.2406 | 66328767.094 | 71430979.9474 | 76533192.8008 | 81635405.6542 | 86737618.5076
Fixed Cost | 3618608.8581 | 3618608.8581 | 3618608.8581 | 3618608.8581 | 5855723.8281 | 5855723.8281 | 5855723.8281 | 5855723.8281 | 8092838.7982 | 8092838.7982 | 8092838.7982 | 10329953.7683 | 10329953.7683 | 10329953.7683 | 10329953.7683 | 12567068.7384 | 12567068.7384 | 12567068.7384
Total Cost | 3618610.5588 | 8720821.7114 | 13823034.5648 | 18925247.4182 | 26264575.2417 | 31366788.0951 | 36469000.9485 | 41571213.8019 | 48910541.6253 | 54012754.4787 | 59114967.3321 | 66454295.1556 | 71556508.009 | 76658720.8623 | 81760933.7157 | 89100261.5392 | 94202474.3926 | 99304687.246
Aluminum has higher total costs compared to steel at all production volumes, primarily due to higher variable costs.
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
20

## Slide 21
SENSITIVITY ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Volume(millions) | Variable | Fixed | Total | No. of Stamping Machine(s)
5 | € 0.62 | 0.72 | 1.34 | 1
10 | € 0.62 | 0.36 | 0.98 | 1
15 | € 0.62 | 0.39 | 1.02 | 2
20 | € 0.62 | 0.29 | 0.92 | 2
25 | € 0.62 | 0.23 | 0.86 | 2
30 | € 0.62 | 0.27 | 0.90 | 3
35 | € 0.62 | 0.23 | 0.87 | 3
40 | € 0.62 | 0.20 | 0.84 | 3
45 | € 0.62 | 0.23 | 0.87 | 4
50 | € 0.62 | 0.21 | 0.85 | 4
55 | € 0.62 | 0.23 | 0.88 | 5
60 | € 0.62 | 0.21 | 0.86 | 5
65 | € 0.62 | 0.19 | 0.85 | 5
70 | € 0.62 | 0.21 | 0.87 | 6
75 | € 0.62 | 0.20 | 0.86 | 6
80 | € 0.62 | 0.19 | 0.85 | 6
85 | € 0.62 | 0.20 | 0.87 | 7
90 | € 0.62 | 0.19 | 0.86 | 7
95 | € 0.62 | 0.18 | 0.85 | 7
100 | € 0.62 | 0.19 | 0.87 | 8
105 | € 0.62 | 0.18 | 0.86 | 8
110 | € 0.62 | 0.20 | 0.88 | 9
115 | € 0.62 | 0.19 | 0.87 | 9
120 | € 0.62 | 0.18 | 0.87 | 9
Chart: Steel
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120
Variable | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657 | 0.61657
Fixed | 0.72362 | 0.36181 | 0.39031 | 0.29273 | 0.23419 | 0.26971 | 0.23118 | 0.20228 | 0.22951 | 0.20656 | 0.22844 | 0.20941 | 0.1933 | 0.21144 | 0.19735 | 0.18501 | 0.20044 | 0.18931 | 0.17934 | 0.19274 | 0.18356 | 0.19555 | 0.18705 | 0.17926
Total | 1.3402 | 0.97838 | 1.0158 | 0.91819 | 0.85965 | 0.90406 | 0.86553 | 0.83663 | 0.87275 | 0.84979 | 0.88057 | 0.86153 | 0.84543 | 0.87246 | 0.85836 | 0.84603 | 0.87035 | 0.85921 | 0.84925 | 0.87153 | 0.86236 | 0.88323 | 0.87473 | 0.86694
Chart: Steel
100 Data points
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
21

## Slide 22
Chart: Aluminum
Chart: Aluminum
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120
Variable | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956
Fixed | 0.72372 | 0.36186 | 0.39038 | 0.29279 | 0.32371 | 0.26976 | 0.29514 | 0.25825 | 0.27927 | 0.25134 | 0.26917 | 0.24674 | 0.22776 | 0.24345 | 0.22722 | 0.24098 | 0.2268 | 0.23906 | 0.22648 | 0.23753 | 0.23203 | 0.24182 | 0.23131 | 0.24032
Total | 2.4192 | 2.0574 | 2.097 | 1.9994 | 2.0414 | 1.9875 | 2.024 | 1.9871 | 2.0192 | 1.9913 | 2.0202 | 1.9978 | 1.9788 | 2.0056 | 1.9894 | 2.0143 | 2.0001 | 2.0235 | 2.0109 | 2.033 | 2.0277 | 2.0486 | 2.0381 | 2.0582
Chart: Aluminum
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120
Variable | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956 | 1.6956
Fixed | 0.72372 | 0.36186 | 0.39038 | 0.29279 | 0.32371 | 0.26976 | 0.29514 | 0.25825 | 0.27927 | 0.25134 | 0.26917 | 0.24674 | 0.22776 | 0.24345 | 0.22722 | 0.24098 | 0.2268 | 0.23906 | 0.22648 | 0.23753 | 0.23203 | 0.24182 | 0.23131 | 0.24032
Total | 2.4192 | 2.0574 | 2.097 | 1.9994 | 2.0414 | 1.9875 | 2.024 | 1.9871 | 2.0192 | 1.9913 | 2.0202 | 1.9978 | 1.9788 | 2.0056 | 1.9894 | 2.0143 | 2.0001 | 2.0235 | 2.0109 | 2.033 | 2.0277 | 2.0486 | 2.0381 | 2.0582
SENSITIVITY ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
100 Data points
Volume(millions) | Variable | Fixed | Total | No. of Stamping Machine(s)
5 | € 1.70 | € 0.72 | € 2.42 | 1
10 | € 1.70 | € 0.36 | € 2.06 | 1
15 | € 1.70 | € 0.39 | € 2.10 | 2
20 | € 1.70 | € 0.29 | € 2.00 | 2
25 | € 1.70 | € 0.32 | € 2.04 | 3
30 | € 1.70 | € 0.27 | € 1.99 | 3
35 | € 1.70 | € 0.30 | € 2.02 | 4
40 | € 1.70 | € 0.26 | € 1.99 | 4
45 | € 1.70 | € 0.28 | € 2.02 | 5
50 | € 1.70 | € 0.25 | € 1.99 | 5
55 | € 1.70 | € 0.27 | € 2.02 | 6
60 | € 1.70 | € 0.25 | € 2.00 | 6
65 | € 1.70 | € 0.23 | € 1.98 | 6
70 | € 1.70 | € 0.24 | € 2.01 | 7
75 | € 1.70 | € 0.23 | € 1.99 | 7
80 | € 1.70 | € 0.24 | € 2.01 | 8
85 | € 1.70 | € 0.23 | € 2.00 | 8
90 | € 1.70 | € 0.24 | € 2.02 | 9
95 | € 1.70 | € 0.23 | € 2.01 | 9
100 | € 1.70 | € 0.24 | € 2.03 | 10
105 | € 1.70 | € 0.23 | € 2.03 | 10
110 | € 1.70 | € 0.24 | € 2.05 | 11
115 | € 1.70 | € 0.23 | € 2.04 | 11
120 | € 1.70 | € 0.24 | € 2.06 | 12
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
22

## Slide 23
LIFE CYCLE IMPACT ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Life Cycle Assessment (Steel)
Material | Unit Cost (EUR/Kg) | Scrap Cost (EUR/Kg) | EI'99 Material Prod | EI'99 EOL | σR | σyeild | Density [kg/m3]
Al | 2.52 | -1.44 | 0.7 | Recycle * -57010^-3 | 290 | 170 | 2712
Steel | 0.72 | -0.17 | 0.55 | Recycle * -9610^-3 | 700 | 350 | 900
Material | Unit Cost (EUR/Kg) | Scrap Cost (EUR/Kg) | EI'99 Material Prod | EI'99 EOL | σR | σyeild | Density [kg/m3]
Al | 2.52 | -1.44 | 0.7 |  | 290 | 170 | 2712
Steel | 0.72 | -0.17 | 0.55 |  | 700 | 350 | 900
Production Phase |  |  | 
Parameter | Tons | Environmental Impact (pts/Kg) | Points
Material | 8399.06 | 0.55 | 4619.48
Scrap(Recycled) | 1449.06 | -0.17 | -246.34
Total |  |  | 4373.14
End Of Life |  |  | 
Pameter | Tons | Environmental Impact (pts/Kg) | Points
Product(Recycle) | 6950 | -0.096 | -667.2
Total Environmental Impact | 3705.94 |  | Pts
Energy Consumption Impact |  |  | 
Pameter | KWh | Environmental Impact (pts/Kg) | Points
Energy Consumption | 1141199.95 | 0.5 | 570599.98
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
26

## Slide 24
LIFE CYCLE IMPACT ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Life Cycle Assessment (Aluminum)
Material | Unit Cost (EUR/Kg) | Scrap Cost (EUR/Kg) | EI'99 Material Prod | EI'99 EOL | σR | σyeild | Density [kg/m3]
Al | 2.52 | -1.44 | 0.7 | Recycle * -57010^-3 | 290 | 170 | 2712
Steel | 0.72 | -0.17 | 0.55 | Recycle * -9610^-3 | 700 | 350 | 900
Material | Unit Cost (EUR/Kg) | Scrap Cost (EUR/Kg) | EI'99 Material Prod | EI'99 EOL | σR | σyeild | Density [kg/m3]
Al | 2.52 | -1.44 | 0.7 |  | 290 | 170 | 2712
Steel | 0.72 | -0.17 | 0.55 |  | 700 | 350 | 900
Production Phase |  |  | 
Parameter | Tons | Environmental Impact (pts/Kg) | Points
Material | 7563.99 | 0.7 | 5294.80
Scrap(Recycled) | 1093.99 | -1.44 | -1575.35
Total |  |  | 3719.44
End Of Life |  |  | 
Pameter | Tons | Environmental Impact (pts/Kg) | Points
Product(Recycle) | 6470 | -0.57 | -3687.9
Total Environmental Impact | 31.54 |  | Pts
Energy Consumption Impact |  |  | 
Pameter | KWh | Environmental Impact (pts/Kg) | Points
Energy Consumption | 1409783.14 | 0.5 | 704891.57
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
27

## Slide 25
LIFE CYCLE IMPACT ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Parameter | Steel(pts.) | Aluminum(pts.) 2
Material | 4619.48 | 10589.59
Scrap(Recycled) | -246.34 | -3150.70
Product(Recycle) EOL | -667 | -7375.8
Total Environmental Impact | 3705.94 | 63.09
Energy Consumption | 570599.98 | 1426499.9
Cummulative points | 574305.92 | 1426563.03
Parameter | Steel(pts.) | 
Material | 4619.48 | 10589.59
Scrap(Recycled) | -246.34 | -3150.70
Product(Recycle) EOL | -667 | -7375.8
Total Environmental Impact | 3705.94 | 63.09
Energy Consumption | 570599.98 | 1426499.9
Cummulative points | 574305.92 | 1426563.03
Chart: 
| Steel | Aluminum
Energy Consumption | 570599.98 | 1426499.9389
Chart: Production Phase
| Steel | Aluminum
 | 4373.14 | 7438.8879
Chart: END OF LIFE
| Steel | Aluminum
 | -667 | -7375.8
Chart: 
| Steel | Aluminum
Cummulative points | 574305.92 | 1426563.0268
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
28

## Slide 26
FUNCTIONAL ASSESSMENT
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Chart: Functional Assesment
| Thermal conductivity | Corrosion resistance | Weight
 | 0.22667 | 0.33 | 0.198
 | 0.34 | 0.165 | 0.33
Importance | Function | Steel | Aluminum
34% | Thermal conductivity | 3 | 4.5
33% | Corrosion resistance | 5 | 2.5
33% | Weight | 3 | 5
1-5 --> 5 is the best
Scores |  | Steel | Aluminum
Thermal Conductivity |  | 23% | 34%
Corrosion Resistance |  | 33% | 17%
Weight |  | 20% | 33%
 | Total | 75% | 84%
Normalization | Steel | Aluminium
Thermal conductivity | 67% | 100%
Corrosion resistance | 100% | 50%
Weight | 60% | 100%
Aluminum
Steel
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
29

## Slide 27
USE PHASE ANALYSIS
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Chart: Use Phase Analysis
| Producton phase | use phase (1st decade) | use phase (2nd decade) | Total Cost over duration
Steel | 0.97838 | 0 | 0 | 0.97838
Aluminum | 2.0575 | 0 | 2.0575 | 4.115
Use Phase Analysis |  | 
 | Alumium Cooker lid | Steel Cooker lid
Duration | 10 years | 20 years
Unitary Cost | € 2.06 | € 0.98
Life Cycle Cost |  | 
Duration (years) | Alumium Cooker lid | Steel Cooker lid
Producton phase | € 2.06 | € 0.98
use phase (1st decade) | € - | € -
use phase (2nd decade) | € 2.06 | € -
Total Cost over duration | € 4.11 | € 0.98
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
30

## Slide 28
TERNARY DIAGRAM
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
Alternatives' Performance | LCC (euros/unit) | LCA (pts/unit) | Functional Assessment
Steel | 0.978 | 0.057 | 7
Aluminum | 4.110 | 0.070 | 9
Normalization of Performance | LCC (euros/unit) | LCA (pts/unit) | Functional Assessment
Steel | 1.00 | 1.00 | 0.78
Aluminum | 0.24 | 0.81 | 1.00
Steel has best scores for higher importance of Environmental and Economical performance
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
31
Aluminum is the best when higher importance is given to Functional performance

## Slide 29
SUMMARY
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
CONCLUSION |  | 
METRIC | STEEL | ALUMINUM
LIFE CYCLE COST (EUROS) | € 98,02,334.74 | € 2,06,25,985.04
LIFE CYCLE IMPACT ANALYSIS (PTS) | 574305.92 | 1426563.03
FUNCTIONAL ANALYSIS (%) | 75% | 84%
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
32
Steel has significantly lower life cycle costs compared to aluminium.
The life cycle impact analysis score is much lower for steel than for aluminium, indicating a smaller environmental impact.
Aluminium has a higher functional analysis percentage, suggesting better performance or efficiency compared to steel.

## Slide 30
THE END
Case Study : Pressure Cooker Lid
Lecturer: Prof. Paulo Pecas
That’s All Folks
TU Chemnitz · Summer Term-2024 · GROUP-4 · Pressure Cooker Lid
LIFE CYCLE ENGINEERING · ADV MANUF
33